(Note to Specifier:  This specification has additional instructions included as Hidden Text.  To view this information, Select Tools, Options, and check Hidden Text in the Formatting Marks section of the View Tab.)

2016 MASTER FORMAT™ SECTION 10 11 00

Schedules for Visual Display Units

3form GLASS MARKERBOARD SYSTEM

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification sections, apply to this Section.

summary

This Section includes the Visual Display Units as shown and specified in the described system(s):

Adjust list below to suit Project

Appliqués

Art Glass

Backsplashes

Markerboard

Moveable Partition

Portable Markerboard

Signage

Sliding Glass Door

Visual Display Surface

Wall Cladding

Wall Paneling

[Insert Item]

Related Sections include the following:

Adjust list below to suit Project

Section 08 32 00 Sliding Glass Doors; Section 08 32 13 Sliding Aluminum-Framed Glass Doors;

Section 10 11 00 Visual Display Surfaces; Section 10 11 16 Markerboards; Section 10 11 16.13 Fixed Markerboards; Section 10 11 16.23 Modular-Support-Mounted Markerboards; Section 10 11 16.33 Rail Mounted Markerboards; Section 10 11 16.43 Portable Markerboards; Section 10 11 33 Sliding Visual Display Units; Section 10 11 33.13 Horizontal-Sliding Visual Display Units; Section 10 11 33.23 Vertical-Sliding Visual Display Units; Section 10 11 36 Visual Display Conference Units; Section 10 11 43 Visual Display Wall Panels;

Section 10 14 00 Signage; Section 10 14 23 Panel Signage;

Section 10 20 00 Interior Specialties;

Section 12 17 00 Art Glass; Section 12 17 13 Etched Glass;

submittals

General:  Submit the following in accordance with conditions of contact and Division 1 specification section 01 33 00 “Submittal Procedures”.

Product Data:  Submit manufacturer’s product data; include product description, fabrication information, and compliance with specified performance requirements.

Shop Drawings: Include plans, elevations, sections, panel dimensions, details, and attachments to other work.

Component Samples for Verification: For each glass product specified: (2) color samples, 4-inch (150-mm) wide x 4-inch (150-mm) long each, representing actual product, color, and finish. For each profile specified: (2) “L” shaped samples to be provided.

Manufacturer’s Certificates: Certify products meet or exceed specified requirements.

Quality Assurance

Installer Qualifications: Approved by manufacturer

quality assurance

Installer’s Qualifications: Approved by manufacturer.

delivery, storage, and handling

Deliver Visual Display Units, systems and specified items in manufacturer’s standard protective packaging.

Do not deliver Visual Display Units, system, components and accessories to Project site until areas are ready for installation.

Store materials in a dry, well ventilated place that is not exposed to exterior elements.

Handle materials to prevent damage to finished surfaces.  Provide protective coverings to prevent damage or staining following installation for duration of project.

Warranty

Provide manufacturer’s (10) year warranty.

PRODUCTS

Manufacturer

Manufacturer:  3form, LLC., Salt Lake City, Utah, USA / telephone 801-649-2500

Manufacturer: EFI, Kernersville, North Carolina, USA/ telephone 800-6687080

VISUAL DISPLAY

** note to specifier ** choose one the following.

Create glass marker boards 1919 (protected edge and face), 2 3/8”w x 13/16”h with 3/16” (4mm) low-iron back-painted glass, seamed edges and fully tempered. Includes wall-mounting hardware. Minimum panel dimensions – 11 ½”w x 7”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1952 (minimal protected edge), 1 ¾”w x 1 ¾”h with a) 1/8”(3mm) or b) 3/16” (4mm) low-iron back-painted glass, polished edges and fully tempered. Mounting hardware provided by others. Minimum panel dimensions – 12”w x 4 1/8”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1960, (continuous mount) 2 3/8”w x 2 3/8”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes wall-mounting hardware. Minimum panel dimensions – 11 ½”w x 7”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1955/1965/1968, (minimal protected edge), 2 3/8”w x 2 3/8”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes mounting hardware. Minimum panel dimensions – 10 1/4”w x 5 13/16”h, maximum panel dimensions 72” x 120”. 10100-3 Magnetic feature

Create glass marker boards, 1960 (floating), 2 11/16”w x 2 11/16”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes mounting hardware. Minimum panel dimensions – 13 ½”w x 7”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1970 (continuous mount), 2 11/16”w x 2 11/16”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes mounting hardware. Minimum panel dimensions – 12 1/4”w x 7 1/4”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1970 (floating), 2 11/16”w x 2 11/16”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes mounting hardware. Minimum panel dimensions – 14 1/4”w x 9 1/4”h, maximum panel dimensions 72” x 120”. Magnetic feature

Create glass marker boards, 1971, (minimal & low profile), 2 11/16”w x 2 11/16”h with 3/16” – ¼” (4 – 6mm) low-iron back-painted glass, polished edges, fully tempered. Includes mounting hardware. Minimum panel dimensions – 12 1/4”w x 7 1/4”h, maximum panel dimensions 72” x 120”. Optional: magnetic feature

Frame / profile finishes: clear anodized, aluminum or white powder coated, aluminum or black powder coated, aluminum or charcoal powder coated, aluminum or dark bronze powder coated, aluminum or grey powder coated, aluminum or nickel powder coated, aluminum.

Glass: select from (99) standard colors at www.efi-us.com/colour-database . Also, custom color matching is available, please inquire by calling 1-800-668-7080.

Hanging hardware (if applicable): as provided by manufacturer to complete installation.

Wall fasteners: provided by others

EXECUTION

examination

Examine substrates, areas, and conditions where installation of Visual Display Units will occur, with Installer present, for compliance with manufacturer’s requirements.  Verify that substrates and conditions are satisfactory for installation and comply with requirements specified.

Install all z-mounting strips, as provided by the manufacturer, to insure the marker board(s) are level and properly secured to the wall to prevent excess movement. All strips should be installed with shims, provided by others, in order to insure the marker boards are installed flat and do not follow the contour of the wall(s).

Verify that structural supports are level and of adequate strength to support the applied loads.

Verify the dimensions prior to assembly and installation.

Notify the Architect of unsatisfactory conditions.

Preparation

Clean the surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

installation

General:  Comply with manufacturer’s written instructions for the installation of Visual Display Units.

Manufacturer’s shop to fabricate items to the greatest degree possible.

Utilize fasteners, adhesives and bonding agents recommended by manufacturer for type of installation indicated.  Material that is chipped, warped, hazed or discolored as a result of installation or fabrication methods will be rejected.

Install components plumb, level and rigid, scribed to adjacent finishes, in accordance with approved shop drawings and product data.

Form field joints using manufacturer’s recommended procedures.  Locate seams in panels so that they are not directly in line with seams in substrates.

We recommend that installation is completed by a 3form Certified Installer. Contact 3form for more information or to get a quote.

cleaning and protection

Protect surfaces from damage until date of substantial completion.  Repair work or replace damaged work, which cannot be repaired to Architect’s satisfaction.

End of Section 06 06 60

Solid Polymer Fabrication #1 (SPF-1)

Product:	[Replace with Collection and product name]

Color:	[Replace with color name]

Gauge:	[1/16"][1/8"][3/16"][1/4"][3/8"][1/2"][3/4"][1"][As indicated on drawings][As required to meet deflection requirements]

Surface Finish:	[Gloss][Soft Etch]

UV Protection is desirable for applications that will receive direct sunlight.

Refer to www.3-form.com for expansion/contraction information.  This information is required for applications subjected to temperature variation.

Orientation: 	[Horizontal][Vertical]

Repeat Product Data Sheets as required to identify all Varia™ applications.